## Slide 1: Microprocessor-Based Product Design
Tutorials 2026/27 · Yohai Ackerman

## Slide 2: Your first STM32 application
TUTORIAL 1 · 2.11.2026
CubeMX configuration, build, flash and run; blink LD2; printf to PuTTY; the debugger: breakpoints, stepping, live expressions; where your code goes (USER CODE sections).

## Slide 3: Your code goes between USER CODE markers
CubeMX generates main.c and the other project files from the .ioc.
Every time you change the .ioc and press Generate Code, the files are rewritten.
Code between USER CODE BEGIN and USER CODE END is kept.
Code anywhere else is deleted, without a warning.
int main(void)
{
/* USER CODE BEGIN 1 */
uint32_t counter = 0; // kept
/* USER CODE END 1 */
HAL_Init();
counter = 5; // DELETED on regenerate
/* USER CODE BEGIN 2 */
...
/* USER CODE END 2 */

## Slide 4: main.c sections before main()
Section | Where it sits | What goes there (example)
Header | File comment at the very top | What the program does, author, date
Includes | #include lines | #include <stdio.h>, your own .h files
PTD | Private typedefs | typedef enum { IDLE, RUN } state_t;
PD | Private defines | #define N_LEDS 8
PM | Private macros | #define SET_BIT_N(x,n) ((x) ¦= 1u << (n))
PV | Private (global) variables | volatile uint8_t state = 0;
PFP | Private function prototypes | static void blinkLed(uint32_t ms);
0 | Your function definitions, before main() | static void blinkLed(uint32_t ms) { ... }
In the file each section looks like /* USER CODE BEGIN PV */ ... /* USER CODE END PV */

## Slide 5: main.c sections inside and after main()
Section | Where it sits | What goes there (example)
1 | Start of main(), before HAL_Init() | Local variables of main()
Init | After HAL_Init(), before the clock setup | Rarely used
SysInit | After the clock setup, before peripheral init | Rarely used
2 | After all MX_..._Init() calls, before the loop | One-time setup: start timers, print a banner
WHILE | Inside while (1), first part | The main loop: your program's work
3 | Inside while (1), after END WHILE | Also runs every pass (CubeMX splits the loop in two)
4 | After main() | Callbacks, e.g. HAL_TIM_PeriodElapsedCallback; more functions
Peripheral init functions have their own sections too, e.g. TIM2_Init 0, 1 and 2.

## Slide 6: PFP: why declare a function before defining it?
The compiler reads the file once, top to bottom.
A function must be declared before the first line that calls it.
A prototype in PFP announces name, inputs and output, so the full definition can come anywhere later.
Bonus: the PFP list is a table of contents of the file.
/* USER CODE BEGIN PFP */
static void blinkLed(uint32_t ms);
/* USER CODE END PFP */
int main(void) {
...
blinkLed(500); // OK: already declared
}
/* USER CODE BEGIN 4 */
static void blinkLed(uint32_t ms) { ... }
/* USER CODE END 4 */

## Slide 7: Header (.h) and source (.c): the same idea across files
io_board.h
Declarations: what exists, how to call it
uint8_t readButtonsRaw(void);
void allRgbOff(void);
io_board.c
Definitions: the code itself
uint8_t readButtonsRaw(void)
{
/* ... HAL_I2C_Mem_Read ... */
}
main.c: #include "io_board.h", the .h only, never the .c
CubeIDE compiles every .c in Core/Src by itself; the linker joins main.o and io_board.o
Including the .c compiles its functions twice: "multiple definition" error

## Slide 8: The same rule in the other generated files
main.h
Includes, ET (exported types), EC (constants), EM (macros), EFP (function prototypes), Private defines. Things other .c files need to see.
stm32g4xx_it.c
Interrupt handlers. Each has sections 0 (before the HAL handler) and 1 (after it). Usually leave them alone and use the HAL callbacks.
Your own files
New .c files in Core/Src and .h files in Core/Inc are never touched by CubeMX. The safest place for larger code.

## Slide 9: Moving a project to another PC
Pack (your PC)
Right-click the project > Refresh (F5)
Right-click > Export > General > Archive File
Untick the Debug folder (build output)
Save as project.zip, Finish
Open (other PC)
File > Import > General > Existing Projects into Workspace
Select archive file > the .zip (do not unzip it)
Tick the project > Finish
Build, then Debug
Project greyed out in the import list? A project with the same name is already in the workspace: delete it first.

## Slide 10: Numbers and bits on the board
TUTORIAL 2 · 9.11.2026
Predict-then-run wrap-around; signed and unsigned in the debugger; a binary printer; the four bit idioms: set, clear, toggle, test.

## Slide 11: RGB LEDs and buttons
TUTORIAL 3 · 16.11.2026
A set_rgb helper; a walking dot with masks; saturating brightness up and down; one press = one action.

## Slide 12: Timer interrupts and PWM
TUTORIAL 4 · 23.11.2026
The ISR and the HAL callback chain; three ways to make a PWM (polling, interrupt, hardware) and what each must fit in time.

## Slide 13: From timer to callback: the whole chain
HARDWARE: runs by itself, costs no CPU time
System clock
170 MHz
Prescaler
divides by PSC + 1
Counter
counts 0 to ARR
Update event
counter wraps to 0
NVIC
raises the interrupt
SOFTWARE: the CPU leaves the main loop, every step costs cycles
ISR
TIM7_DAC_IRQHandler
HAL handler
checks and clears the flag
Your callback
PeriodElapsedCallback
Main loop
continues where it stopped
finterrupt = fclk / ((PSC + 1) · (ARR + 1)) Tperiod = 1 / finterrupt
CPU share used = tISR / Tperiod (tISR: one pass through ISR + HAL handler + callback)

## Slide 14: The ISR: what runs when an interrupt fires
An interrupt is a hardware event (a timer period ends, a pin changes, a byte arrives) that pauses the main loop.
The CPU runs one function, the ISR (Interrupt Service Routine), then returns to where it stopped.
The NVIC finds the ISR in the vector table. CubeMX writes it in stm32g4xx_it.c; it calls the HAL, which calls your callback.
Entering and leaving costs about a dozen cycles each way, plus the HAL code.
Keep it short: no HAL_Delay, printf or I2C. Set a counter or a flag; the main loop does the rest.
/* stm32g4xx_it.c: the ISR (CubeMX) */
void TIM7_DAC_IRQHandler(void)
{
HAL_TIM_IRQHandler(&htim7);
}
/* HAL: checks and clears the flag, */
/* then calls the callback */
/* main.c: your callback */
volatile uint32_t ticks = 0;
void HAL_TIM_PeriodElapsedCallback(
TIM_HandleTypeDef *htim)
{
if (htim->Instance == TIM7)
ticks++; /* short! */
}

## Slide 15: Three ways to make a PWM
 | 1. Polling main loop reads HAL_GetTick() | 2. Interrupt TIM7 callback, once per period | 3. Hardware TIM2 compares CNT with CCR
Who compares | the main loop, once per pass | the callback, once per period | the timer itself, on every count
Code | pwm = (HAL_GetTick() % N) < M; HAL_GPIO_WritePin(..., pwm); | step = (step + 1) % N; HAL_GPIO_WritePin(..., step < M); | TIM2->CCR1 = M; once; ARR = N − 1 is set in CubeMX
Step counter | HAL_GetTick() % N; tstep = 1 ms, the pin changes once per loop pass | step, +1 per callback; tstep = Tperiod of TIM7 | CNT itself, 0 to ARR; tstep = ttick
PWM cycle TPWM | N · 1 ms, if a loop pass is much shorter than 1 ms | N · Tperiod | N · ttick = (ARR + 1) · ttick
CPU cost | the whole CPU (slide 16) | tISR / Tperiod (slide 17) | zero (slide 18)
Breaks when | any code makes the loop longer: the edges jitter by one loop pass | Tperiod comes close to tISR: fine steps or a fast PWM | the pin is not a timer channel pin
One PWM cycle: a step counter goes 0, 1, ..., N − 1 and jumps back to 0. The output is on while the counter is below M.
N: steps per cycle. M: steps on. tstep: one step. TPWM = N · tstep, fPWM = 1 / TPWM, duty = M / N. Each method gets its step counter from a different source.
The CPU can read a counter at any moment, but it is never interrupted at each count.
HAL_GetTick() changes every 1 ms. TIM2->CNT changes every ttick (5.9 ns at PSC = 0), but the loop sees it only once per pass, so the step becomes tloop.

## Slide 16: Polling: what must fit in one step
Symbol | What it is | Formula | Working example fPWM = 100 Hz, N = 10 | Not working example fPWM = 100 Hz, N = 10
tstep | One PWM step | HAL_GetTick(): fixed | 1 ms | 1 ms
M | Steps on, for 50 % | N / 2 | 5 | 5
TPWM | PWM cycle | N · tstep | 10 ms | 10 ms
tloop | One pass of the main loop | cycles · tclk: measure it | about 1 µs: PWM lines only | about 1.9 ms: plus a printf
tlate | How late an edge can be | up to tloop | 1 µs | 1.9 ms
duty | Duty you get | M / N | 50 % | 31 to 69 %
Must hold: tloop much shorter than tstep. Every line in the loop (printf, I2C, HAL_Delay) adds to tloop.
Working example: fPWM = 100 Hz, N = 10
HAL_GetTick() goes up by 1 every 1 ms: that is one PWM step.
One pass of the loop takes about 1 µs, so the loop reads each tick value about 1000 times.
HAL_GetTick() % 10 is the step counter: 0, 1, ..., 9, then back to 0. One cycle lasts 10 ms (100 Hz).
For steps 0 to 4 (below M = 5) the pin is on, 5 ms; for steps 5 to 9 it is off.
Each change is seen at most 1 µs late, so the duty stays 50 %.
Not working example: fPWM = 100 Hz, N = 10
The same PWM, plus one printf of 22 characters in the loop.
At 115 200 baud a character takes 87 µs, so the printf blocks for 22 · 87 µs ≈ 1.9 ms.
One pass now takes 1.9 ms: the loop reads the tick only about every second step.
The pin changes up to 1.9 ms late: the 5 ms on time becomes anything from 3.1 to 6.9 ms.
The duty jumps between 31 and 69 % from cycle to cycle: the LED flickers.

## Slide 17: Interrupt: what must fit in one period
Symbol | What it is | Formula | Working example fPWM = 1 kHz, N = 100 | Not working example fPWM = 20 kHz, N = 100
PSC, ARR | TIM7 prescaler and auto-reload | set in CubeMX | 169, 9 | 16, 4
ttick | One count of TIM7 | (PSC + 1) · tclk | 170 · 5.9 ns = 1 µs | 17 · 5.9 ns = 0.1 µs
Tperiod | Between interrupts: one step | (ARR + 1) · ttick | 10 · 1 µs = 10 µs | 5 · 0.1 µs = 0.5 µs
M | Steps on, for 50 % | N / 2 | 50 | 50
tISR | CPU time of one interrupt | cycles · tclk: measure it | 170 cycles = 1 µs | 1 µs
tfree | Left for the main loop | Tperiod − tISR | 9 µs (90 %) | 0.5 − 1 < 0: none
TPWM | PWM cycle | N · Tperiod | 1 ms | about 100 µs, not 50 µs
Must hold: tISR < Tperiod, with a margin: keep tISR below about 10 % of Tperiod.
Working example: fPWM = 1 kHz, N = 100
TIM7 counts every 1 µs (PSC = 169) and wraps after 10 counts (ARR = 9): an interrupt every 10 µs, which is one PWM step.
After 0.07 µs (12 cycles) the CPU is in the ISR. HAL clears the flag, and the callback runs step = (step + 1) % 100 and sets the pin on while step < 50.
About 1 µs after the wrap the CPU is back in the main loop, with 9 µs (90 %) left.
100 steps of 10 µs make one cycle: 1 ms, so 1 kHz at 50 %.
Not working example: fPWM = 20 kHz, N = 100
For 20 kHz with 100 steps, one step must last 50 µs / 100 = 0.5 µs: PSC = 16 (0.1 µs per count) and ARR = 4.
One interrupt takes about 1 µs, so the next wrap comes before the ISR ends.
The CPU re-enters the ISR at once and the main loop never runs: no printf, no buttons.
The flag cannot count twice, so every second interrupt is lost: step counts at half speed, and TPWM ≈ 100 µs (10 kHz).

## Slide 18: Hardware: what limits the PWM
Symbol | What it is | Formula | Working example fPWM = 17 kHz, N = 10 000 | Not working example fPWM = 100 kHz, N = 10 000
TPWM | PWM cycle | 1 / fPWM | 59 µs | 10 µs
ttick | One count of CNT: one step | TPWM / N | 5.9 ns | 1 ns: shorter than tclk
PSC | Prescaler | ttick / tclk − 1 | 0 | 0.17 − 1 < 0: impossible
ARR | Auto-reload | N − 1 | 9999 | 9999
M | CCR, for 50 % | N / 2 | 5000 | 5000
CPU | CPU time per cycle | none | 0 | 0
Must hold: fPWM · N ≤ fclk = 170 MHz. The CPU is never involved: no tISR, no tloop.
Working example: fPWM = 17 kHz, N = 10 000
17 kHz means one cycle of 1 / 17 kHz = 59 µs. With N = 10 000, one step lasts 59 µs / 10 000 = 5.9 ns: exactly one clock, so PSC = 0 and ARR = N − 1 = 9999.
TIM2’s counter CNT counts 0 to 9999, one count per 5.9 ns, and wraps. The code writes TIM2->CCR1 = 5000 once.
On every count the timer compares CNT with CCR: the pin is on for counts 0 to 4999 (29.5 µs) and off for the rest. No code runs, the CPU is free.
Not working example: fPWM = 100 kHz, N = 10 000
100 kHz means one cycle of 10 µs. With the same N = 10 000, one step would last 10 µs / 10 000 = 1 ns.
The shortest step is one clock, 5.9 ns. 1 ns would need PSC + 1 = 0.17, which is impossible.
The check: 100 kHz · 10 000 = 1 GHz, more than fclk = 170 MHz.
With PSC = 0 and ARR = 9999 the timer gives only 17 kHz. For 100 kHz, N must drop to 1700 (ARR = 1699).

## Slide 19: Inside the I2C bus
TUTORIAL 5 · 30.11.2026
I2C bus scan: detect the five IO-board chips; set_rgb rewritten on raw HAL_I2C_Mem_Write; servo sweep. Short part: creating a .ioc in STM32CubeMX, and starting Assignment 2 from it.

## Slide 20: From a .ioc to a running project
1. Configure
STM32CubeMX, file ass1.ioc
The whole hardware setup: pins, peripherals, clock, interrupts
2. Generate
GENERATE CODE writes main.c with MX_GPIO_Init(), MX_I2C1_Init(), ...
and copies the HAL drivers
3. Import and code
STM32CubeIDE: File > Import, then the wizard STM32CubeMX/ STM32CubeIDE Project
Your code goes only between USER CODE BEGIN and END
The .ioc is the source. Every GENERATE CODE rewrites the generated code and keeps only what is inside the USER CODE sections.

## Slide 21: Rebuilding ass1.ioc: board and pins
What | Where in CubeMX | Set
Board | File > New Project > Board Selector | NUCLEO-G474RE; answer Yes to initialise all peripherals with their default mode (gives LD2, B1, LPUART1 and the debug pins)
IR sensor | Pinout view: click PA7 | GPIO_Input; right-click > Enter User Label: IR_SENSOR
I2C1 | Connectivity > I2C1 > Mode: I2C | Check the pins: PB8 = SCL, PB9 = SDA. Ctrl+click a pin to see where else it can go
Debug pins | PA13, PA14, PB3 | Never reassign them: they connect the ST-LINK debugger
A user label becomes a name in main.h: IR_SENSOR_Pin, IR_SENSOR_GPIO_Port.

## Slide 22: Peripherals, clock and interrupts
What | Where in CubeMX | Set
I2C1 | Connectivity > I2C1 > Parameter Settings | Standard mode, 100 kHz
LPUART1 | Connectivity > LPUART1 | Asynchronous, 115200 baud, 8 bits, no parity, 1 stop bit
Clock | Clock Configuration tab | HCLK = 170 MHz (PLL from HSI)
B1 interrupt | System Core > NVIC | EXTI line[15:10] interrupts: Enabled
Project | Project Manager tab | Name ass1, Toolchain / IDE: STM32CubeIDE. Then GENERATE CODE
Check: main.c calls MX_GPIO_Init(), MX_LPUART1_UART_Init() and MX_I2C1_Init(), the same as the provided ass1.ioc.

## Slide 23: Assignment 2: start from ass1.ioc
Duplicate
Open ass1.ioc in STM32CubeMX
File > Save Project As
Choose a new folder named ass2: you get ass2.ioc
ass1.ioc stays unchanged
Add only what is new
Motors: TIM2 PWM CH1 to CH4, four DIR pins
Encoders: TIM1, TIM8, TIM3, TIM4 in encoder mode
Ultrasonic: TIM5 (TRIG by PWM, ECHO by input capture)
GENERATE CODE, then import the ass2 folder
Leave the Assignment 1 settings as they are. The full list is in the Assignment 2 configuration section of the assignment sheet.

## Slide 24: Blocking vs. non-blocking
TUTORIAL 6 · 7.12.2026
Registers on another chip vs. in RAM; one ultrasonic distance measurement; an EXTI interrupt with a counter.

## Slide 25: Why some outputs are fast and others slow
Wheel PWM: TIM2->CCR1 = value;
~20 ns
The register is inside the STM32. It has a memory address, so one store instruction over the internal bus writes it: a few clock cycles at 170 MHz (1 cycle = 5.9 ns). TIM2 then makes the PWM by itself.
LED brightness: HAL_I2C_Mem_Write
~0.3 ms
The register is inside the PCA9634, another chip. The only way in is the I2C bus at 100 kHz: 10 µs per bit. Address + register + data, each with an ACK, is about 29 bits. The CPU waits all that time.

## Slide 26: Blocking: updating all 24 LED registers at once
for (ch = 0; ch < 8; ch++) {
setLedChannel(RED, ch, r); // 0.3 ms
setLedChannel(GREEN, ch, g); // 0.3 ms
setLedChannel(BLUE, ch, b); // 0.3 ms
}
// about 7 to 9 ms with the loop stuck here
While stuck, the main loop cannot:
see a new command or state
poll the IR obstacle sensor (an emergency stop!)
run the state's work or print status
Interrupts still run: TIM2 keeps the PWM going and TIM5 still captures the ultrasonic echo.

## Slide 27: Non-blocking: one register per loop pass
static void serviceRgbOutputs(void)
{
if (micros() - lastUs < 1200) return;
lastUs = micros();
/* write ONE of the 24 registers */
setLedChannel(chip, channel, target);
index = (index + 1) % 24;
}
The logic writes the wanted colours into RAM arrays (rgbTarget...): instant.
serviceRgbOutputs copies them to the chips, at most one register per call.
Each loop pass pays at most 0.3 ms; a full refresh takes 24 x 1.2 ms = 29 ms, too fast for the eye.
What makes it non-blocking is the work per call, not where the call is placed.

## Slide 28: Three layers: decide, store, transport
Layer | Wheels | RGB LEDs
Logic: what should the output be now? | runStateTick calls setWheelPwm(wheel, pwm) | runStateTick calls updateLedBlink / updateLedFade
Stored value | TIM2 CCR register (on chip) | rgbTarget arrays (RAM)
Transport: make the hardware show it | TIM2 hardware, continuously, no code | serviceRgbOutputs over I2C, gradually
serviceRgbOutputs is the software stand-in for what TIM2 does for the wheels. It belongs to the transport layer, so it is not part of runStateTick.

## Slide 29: The super loop: inputs, logic, services
while (1)
{
updateEncoders(); /* 1. inputs */
updateIrSensor();
if (state != applied) /* 2. logic */
enterState(state); /* once */
runStateTick(applied); /* every pass */
serviceRgbOutputs(); /* 3. services */
printPeriodicStatus();
}
Keep every pass short, so polled inputs stay responsive.
runStateTick: what the current state wants.
Services: make the hardware match, in every state.
Calling a service from inside one state's case would freeze that output in all other states.

## Slide 30: One wheel in the air
TUTORIAL 7 · 14.12.2026
Open-loop PWM; encoder counts to rad/s; record a run and export it to MATLAB.

## Slide 31: Different encoder configurations
TUTORIAL 8 · 21.12.2026
Encoder mode TI1 vs. TI1 and TI2: counts per revolution, resolution and count direction.

## Slide 32: From model to PI controller
TUTORIAL 9 · 28.12.2026
Model fit, sisotool, c2d; the difference equation in C; simulated vs. measured step response.

## Slide 33: Kinematics (straight lines) and state machine
TUTORIAL 10 · 4.1.2027
Wheel speeds for driving in straight lines; a state machine (enum + switch) for a driving sequence.

## Slide 34: Simulink to C
TUTORIAL 11 · 11.1.2027
Export a Simulink PI controller or filter to C and run it on the cart.

## Slide 35: Project clinic
TUTORIAL 12 · 18.1.2027
Open session for Assignment 3 questions.

## Slide 36: Lab meeting
SESSION 13 · 25.1.2027
Open questions.